## Slide 1: dbcAmplicons pipeline Amplicons
Matthew L. Settles
Genome Center Bioinformatics Core
University of California, Davis
settles@ucdavis.edu; bioinformatics.core@ucdavis.edu

## Slide 2: Amplicons: Common Approach (among many)
Common approach
Single PCR
Long primer sequences (~75bp) that contain barcodes and sequencing adapters
Single or dual barcodes
  (dual barcode often within read 2)

## Slide 3: dbcAmplicons
Originally conceived in late 2012 to lower per sample costs on relatively short targeted (PCR) regions
  16S, ITS, LSU, 18S, etc. Community profiling
  Extraction of mitochondria, virae, chloroplast regions, plasmids by PCR
  Genotyping of samples for phylogenomics, genome to phenotype interactions
Uses the Illumina platform, capably of pooling thousands, or even tens of thousands of barcoded samples/targets per sequencing run.
Core Facility friendly, facilitates interactions between and across individual labs, standardizing workflows.

## Slide 4: Amplicons: Two Step PCR Approach
Barcodes and adapters are added in the second round of PCR
PCR-1
Template with overhang
PCR-2
Add barcodes and adapters

## Slide 5: Amplicon sequencing with dual barcoding
2-step PCR, where the first PCR extracts out the target specific region and the second PCR add on adapters and barcodes. Target specific primers include universal sequences CS1 and CS2, the second PCR extends the universal sequences with adapters and barcodes.
Adapters and barcodes are not included in the target specific primers which allows for maximum flexibility in target specific primer usage and the ability to swap out targets, or include multiple targets in the same sequencing reaction without needing to purchase a large number of barcoded, target specific primers.
Barcodes are included in both adapters, therefor a pair of barcodes are used to uniquely identify a samples. This allows for 32 barcode pairs to be able to uniquely identify 1024 samples.

## Slide 6: Multiplex Samples
Dual barcoding allows for massively multiplexing of samples using only a relatively few primers
GTATCGTC
TGCTCGTA
GTCGTCGT
GTGCGTGT
GCGTCGTG
GTCGTGTA
GATGTAGC
GAGTGATC
CGCTATCA
CGCTGTAG
Pairing of BC1 and BC2 uniquely identifies sample
5 Pairs of Barcodes allows for multiplexing of 25 samples.
32 Pairs can multiplex 1024 samples in the same sequencing reaction
8bp [Error-Correcting]
Barcodes

## Slide 7: Multiplex Amplicon Targets
48 samples X 48 amplicons
2304 Two-step PCR reactions
PCR-1 product
PCR-2 product
Fluidigm Access Array System
Pool many samples

## Slide 8: Primer Design

## Slide 9: Template Specific Primer Design
Each primer pair contains the following parts
  CS1 or CS2 to attach second adapter/barcode primer
  Phase-shifting bases [see below]
  Linker sequence
  Template specific primer sequence
TCA
GTCA
AGTCA
Phase shifting primer
TS
CS
CA
NCA
NNCA
NNNCA
Phase shifting primers with PCR duplicate detection
TS
CS
CA
Ns, resolve to be PCR duplicate keys and should only ever appear once

## Slide 10: Components of the target specific primer
CS1, or CS2 sequence (Nextera sequences)
  Provides the sequence necessary for priming of PCR-2, also serves as the sequencing primer site
Phase-shifting bases
  Generates diversity in the sequencing reaction
Linker sequence
  Buffers the target specific primer sequence from the rest of the primer, preventing some taxa (longer priming) from being more efficient than others.
Target specific primer sequence

## Slide 11: Example target specific primers
Example 27F and 534R (red bases are the inserted bases)
ID | Primer
CS1-27F | TCGTCGGCAGCGTCAGAGTTTGATCCTGGCTCAG
CS1-27F_2 | TCGTCGGCAGCGTCCAGAGTTTGATCCTGGCTCAG
CS1-27F_3 | TCGTCGGCAGCGTCTCAGAGTTTGATCCTGGCTCAG
CS1-27F_4 | TCGTCGGCAGCGTCGTCAGAGTTTGATCCTGGCTCAG
ID | Primer
CS2-534R | GTCTCGTGGGCTCGGATTACCGCGGCTGCTGG
CS2-534R_2 | GTCTCGTGGGCTCGGCATTACCGCGGCTGCTGG
CS2-534R_3 | GTCTCGTGGGCTCGGTGATTACCGCGGCTGCTGG
CS2-534R_4 | GTCTCGTGGGCTCGGGCGATTACCGCGGCTGCTGG
CS1/CS2 sequence, Phase-shifting bases, Linker sequence, target specific primer

## Slide 12: Components of the Barcoded adapter primers sequence
P5, or P7 sequence
  Primers to the Illumina flow cell, Sequence on the P5 strand typically constitutes R1, those on P7 strand typically constitutes R2.
Barcode sequence
  Uniquely identifies sample
CS1, or CS2 sequence (Nextera sequences)
  Necessary for extending PCR-1

## Slide 13
Example barcoded adapter primers
Example 27F and 534R (red bases are the inserted bases)
ID | Primer
P5-Index1-CS1 | AATGATACGGCGACCACCGAGATCTACACTAGATCGCTCGTCGGCAGCGTC
P5-Index2-CS1 | AATGATACGGCGACCACCGAGATCTACACCTCTCTATTCGTCGGCAGCGTC
P5-Index3-CS1 | AATGATACGGCGACCACCGAGATCTACACTATCCTCTCGTCGGCAGCGTC
P5-Index4-CS1 | AATGATACGGCGACCACCGAGATCTACACAGAGTAGATCGTCGGCAGCGTC
ID | Primer
P7-Index1-CS2 | CAAGCAGAAGACGGCATACGAGATTAAGGCGAGTCTCGTGGGCTCGG
P7-Index2-CS2 | CAAGCAGAAGACGGCATACGAGATCGTACTAGGTCTCGTGGGCTCGG
P7-Index3-CS2 | CAAGCAGAAGACGGCATACGAGATAGGCAGAAGTCTCGTGGGCTCGG
P7-Index4-CS2 | CAAGCAGAAGACGGCATACGAGATTCCTGAGCGTCTCGTGGGCTCGG
P5/P7 sequence, Barcode, CS1/CS2 sequence

## Slide 14: QC: what is a “good” library?
Unused primers and adapters
BAD!
Good!
Unused primer
Template of interest

## Slide 15: Pooling Samples/Amplicons
Even amplicon representation is important and difficult to achieve. Amplicon counts can vary from sample to sample by 100x
Each amplicon should be evaluated by quality (ideally by trace) and quantity (fluorometer). Both qualities will effect final counts.
Best practices
  First group amplicons by quality/quantity profiles
  Pool each group separately
  If a small number of groups consider qPCR on each group for final pooling concentrations
  If a large number re-quantify and pool to final pool.

## Slide 16: Benefits/Drawbacks
Drawbacks
Benefits
Maximum Flexibility, fewer target specific primers needed.
Dual barcoding, allowing for massively multiplexing of samples to occur.
Pool multiple targets per run
Software for demultiplexing
Two – step PCR reaction
Sequence the target specific primer

## Slide 17: Nucleotide diversity
Critically important for imaging clusters

## Slide 18: Nucleotide Diversity
Once a sample library is converted to clusters on a flow cell, “nucleotide diversity” refers to the distribution of nucleotides across the flow cell at any given cycle. From the viewpoint of the instrument software, a high diversity library translates into analyzing images containing an even distribution of spots from 4 different color channels corresponding to the 4 nucleotide bases A, T, C & G. In contrast, an unbalanced nucleotide distribution or “low diversity library” means that for any given image, or to two bases are present at a high percentage

## Slide 19: Low Diversity Library vs High Diversity Library
Low Diversity Library
High Diversity Library

## Slide 20: Ways to ensure nucleotide diversity
Appropriate nucleotide diversity and cluster density are important for high quality data. Low nucleotide diversity in combination with high cluster density will most-likely lead to poor data quality and/or low data yield.
Ways to avoid low nucleotide diversity
Sequence the sample at a 30-40% lower density
Spiking in at a 5-50% a nucleotide balanced library
(such as PhiX, or better a shotgun library of a sample of interest)
Multiplex a high number of amplicon regions 12 or greater)
Build phase-shifted primers
Note: Experience has shown, that 15% shotgun spike-in, plus phase-shifted primers and/or multiple target region typically yields good results.

## Slide 21: Illumina Sequencing Requires custom sequencing primers to be added to the reaction (Typical Illumina sequencing primers remain in the reaction for sequencing of PhiX or other shotgun library)
Read | Sequencing Primers
Read1 primer | Illumina Primers
Read2 primer | Illumina Primers
BC1 primer | Illumina Primers
BC2 primer | Illumina Primers
Target Sequence
CS1
CS2
BC1
P7
BC2
P5
Read1 (300bp)
Read1 primer
Read2 (300bp)
Read2 primer
BC1 (8bp)
BC2 (8bp)
BC2 primer
BC1 primer

## Slide 22: Common Analysis Workflow
Identify barcodes
Identify primer sequence (if present) and trim
Overlap paired end reads to produce single read, full amplified target sequence
Generate operational taxonomic unites (“OTUs”), via clustering or classification
Assign ”OTUs” to an organism
Generate abundance tables
Statistical testing

## Slide 23: Common workflows
Qiime
  Now uses Data2
Mothur
Dada2
dbcAmplicons (my software)

## Slide 24: dbcAmplicons
Target Specific
Primer Design
Primer Validation
Dual-barcoded
Two-step
PCR
DNA
Pooling
And
Quantification
Illumina Sequencing
Four Read Setup
Preprocess:
Demuliplex by barcodes and primer sequences
Downstream
Analysis
Performed in Researcher’s Lab
Python dbcAmplicons application
Performed in Core Facility
Two-step PCR
highly multiplexed and modular amplicon design